## Slide 1: Application Aware Routing in SDN
Abhishek Jain
Anish Achuthan
Srikar Durbha

## Slide 2: Introduction
Traditional networks were designed to forward packets from source to destination using the shortest route possible. Routers and switches were mostly agnostic to the applications being served by the network
Today’s networks are forced to be application-aware, to improve user experience, provide service differentiation, and reduce operational costs.

## Slide 3
Software-defined network (SDN) architecture allows service providers to build networks with increased application awareness, which can be built into the network by developing SDN controller applications that keep track of application-level characteristics and use that intelligence to provision flow into the network switches.

## Slide 4
Sender
S 1
S 3
S 4
S 5
S 6
S 7
S 2
Receiver
HTTP
UDP
ICMP
FTP
TCP
HTTP
UDP
ICMP
FTP
TCP
SDN Controller

## Slide 5: Methodology
When the client transmits an IP packet, the switch inspects the packet and depending on the policy/rule installed in it, forwards the packet on a particular route.
If the switch doesn’t have any policy/rule installed, it sends the packet to the controller. The controller inspects the packet header and/or the payload determines the type of packet(TCP,UDP,HTTP…) and installs a policy/rule on the switch instructing it to forward packets along a particular route.

## Slide 6: Our Implementation
We have created different paths for TCP, UDP and ICMP traffic.
We have further classified TCP traffic in to HTTP and FTP traffic.
For each of this different types of traffic we have assigned them a dedicated path.

## Slide 7: POX Implementation
When the switch forwards the packet it receives to the controller, the controller checks the Ethernet packet for IP content.
If its indeed an IP packet, the controller then checks the protocol header to determine if it’s a TCP, UDP or an ICMP packet.
If the packet is a TCP packet, then it further determines if the packet is HTTP or FTP by inspecting the port number.

## Slide 8
After the controller determines the type of packet, it instructs the switch to send the packet along a specific path/route.
According to our topology:
    TCP packets are routed along S7
    UDP packets are routed along S4
    ICMP packets are routed along S5
    HTTP packets are routed along S3
    FTP packets are routed along S6

## Slide 9: C++ Implementation
We have also performed Deep Packet Inspection(DPI) using C++ where a similar topology was used wherein the controller installs a rule on the switch, instructing it to forward the packets along the different paths depending on the type of the packet.
The controller inspects the Ethernet packet for IP content and further for TCP, UDP and ICMP content based on the protocol header.
TCP packets are further inspected for HTTP and FTP traffic by performing a string search in the payload for keywords(HTTP 1.1 for HTTP traffic and FTP/SFTP for FTP traffic)

## Slide 10: THANK YOU